## Slide 1: Intro to Computer Science
Basis for the Design and Use of Computers
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Table of Contents
Early Computing
Boolean Logic and Logical Gates
ALU (Arithmetic and Logic Units)
Registers, RAM
CPU - Instruction Cycle

## Slide 3: Have a Question?
sli.do
#fund-common

## Slide 4
Early Computing

## Slide 5: The Abacus
Calculating tool that was in use in Europe, China and Russia
Originally, they were beans or stones moved in grooves in sand or on tablets of wood, stone, or metal

## Slide 6: The Punched Card
Piece of stiff paper that can be used to contain digital data represented by the presence or absence of holes in predefined positions
Widely used through much of the 20th century in the data processing industry

## Slide 7: Transistors
Used to amplify or switch electronic signals and electrical power
Has at least three terminals for connection to an external circuit
The transistor is the fundamental building block of modern electronic devices

## Slide 8
Structure of Transistors

## Slide 9
Boolean Logic
Abstraction
level:
1 2 3 4 5

## Slide 10: Boolean Algebra
Branch of algebra in which the values of the variables are the truth values true and false, usually denoted 1 and 0 respectively
Formalism for describing logical relations
There are 4 logical operations:
  NOT
  AND
  OR
  XOR

## Slide 11: NOT Operation
Takes a single value True or False and flips it
NOT gate:
output output
input input
Input | Output
True | False
False | True
on
off
on
off

## Slide 12: AND Operation
Takes two input values and outputs a single value
Input A | Input B | Output
True | False | False
False | True | False
True | True | True
False | False | False

## Slide 13: AND Gate
current
output
Input A
Input B
on
off
off
current
output
on
on
on
Input A
Input B

## Slide 14: OR Operation
Takes two input values and outputs a single value
Input A | Input B | Output
True | False | True
False | True | True
True | True | True
False | False | False

## Slide 15: OR Gate
current
output
Input A
Input B
on
off
on

## Slide 16
Logical operations notation
NOT:
AND:
OR:
From now on, we are going to use them like this

## Slide 17
Abstraction
level:
1 2 3 4 5
Logic Gates

## Slide 18: XOR Operation
Takes two input values and outputs a single value
XOR is OR but not AND
Input A | Input B | Output
True | False | True
False | True | True
True | True | False
False | False | False

## Slide 19: Problem: XOR Gate
Try to recreate how the XOR gate will look like
XOR is OR but not AND, so:
  Include OR
  Include AND
  Include NOT after the AND
  Connect all of them with AND

## Slide 20: Solution: XOR Gate
Input A
Input B
XOR notation:
Output
AND
NOT
OR
AND
XOR

## Slide 21
Arithmetic and Logic Units
ALU
Abstraction
level:
1 2 3 4 5

## Slide 22: What is ALU
Electronic circuit that performs arithmetic and bitwise operations on integer binary numbers
To sum binary numbers, we use the following:
To carry over we use AND gate
0 + 0 = 0
1 + 0 = 1
0 + 1 = 1
1 + 1 = 0 (1)
We carry over the 1
This is actually XOR

## Slide 23: Half Adder
So to represent adding binary numbers we use XOR + AND
Half Adder notation:
sum
carry
Input A
Input B
AND
XOR
HA
InA
InB
C
S

## Slide 24: Full Adder
To sum binary numbers, we have to send that 1 that we carried over to the next column
To do that, we just need to take that carried over 1 and send it as input to another half adder
We need two half adders to create full adder

## Slide 25: Problem: Full Adder
Knowing what a half adder is, try creating full adder (used for carrying over ones)
Full adder is chaining two half adders:
  Take a half adder
  Make its sum an input to another half adder
  The other input of the second adder will be a carry (if one)
  Then add an OR gate to calculate the carry of the two half adders

## Slide 26: Solution: Full Adder
HA
InA
InB
C
S
HA
InA
InB
C
S
C
OR
C
So a full adder receives 3 inputs and produces two outputs (sum and carry)
Full Adder notation:
OPCODE – 4-bit code to determine the operation (1000 – Add, 1100 - Subtract)
STATUS – 3 outputs (zero, negative, overflow).

## Slide 27
Registers, RAM
Abstraction
level:
1 2 3 4 5

## Slide 28: Gated Latch
Circuit that has two stable states and can be used to store state information
It has a third input that must be active for the SET and RESET inputs to take effect
This third input is sometimes called ENABLE because it enables the operation of the SET and RESET inputs

## Slide 29: Gated Latch Structure
When turning Write enable on, we save the output
Input
Output
Write
enable
AND
AND
AND
NOT
NOT
OR
GL
In
WE
Out

## Slide 30: 8-bit Registers
D - data in
E - write enable
Q - data out
1
1
1
0
0
Q
D E
Q
D E
Q
D E
Q
D E
Q
D E
1
1
1
1
0
0

## Slide 31: Multiplexer
Grid of many latches
Selects one of several analog or digital input signals and forwards the selected input into a single line
Is used to increase the amount of data that can be sent over the network
Multiplexers can also be used to implement Boolean functions of multiple variables
RAM contains many multiplexers

## Slide 32: RAM
Stores data and machine code currently being used
Allows data items to be read or written
Address | Data
0 | 001001
1 | 010010
2 | 011011
3 | 011101
4 | 101001
5 | 110110
… | …
8-bit data
8-bit address input
Write enable
Read enable

## Slide 33
CPU and Instruction cycle
Abstraction
level:
1 2 3 4 5

## Slide 34: What is a CPU?
Carries out the instructions of a computer program by performing the basic arithmetic, logical, control and input/output (I/O) operations
Fundamental operation of most CPUs is to execute a sequence of stored instructions that is called a program

## Slide 35: Instructions Table
Instruction | Description | 4-bit opcode | Address/Register
LOAD_A | Read RAM location into register A | 0010 | 4-bit RAM address
LOAD_B | Read RAM location into register B | 0001 | 4-bit RAM address
STORE_A | Write from register A into RAM location | 0100 | 4-bit RAM address
ADD | Add two registers and store into second register | 1000 | 2-bit register ID, 2-bit register ID

## Slide 36: Example
RAM | 
Address | Data
0 | 00101000
1 | 00011111
2 | 10000100
3 | 01001101
4 | 00000000
5 | 00000000
6 | 00000000
7 | 00000000
8 | 00100101
9 | 00000011
10 | 00001110
… | …
Register A
00000000
Register B
00000000
Register C
00000000
Register D
00000000
Instruction Address Register
00000000
Instruction Register
00000000
Fetch Phase
Instruction Register
00101000
Decode Phase
Instruction Register
00101000
Opcode
Instruction Register
00101000
RAM Address
LOAD_A
8
Register A
00100101
Execute Phase
Instruction Register
00101000

## Slide 37: What to discuss
Discuss how addition will work in the CPU
Try adding ALU in the system
How will ALU be used
How will multiplication and division work
How will if-statements and for-loops work

## Slide 38
Live Exercises

## Slide 39: Summary
…
…
…
Computer science forms the basis for the design and use of computers
Transistors and logic gates are the basics in computing
Latches build Multiplexers, which build RAM
All the operations in the CPU are build on top of logical operations

## Slide 40
https://softuni.bg/courses/programming-fundamentals

## Slide 41: SoftUni Diamond Partners

## Slide 42: SoftUni Organizational Partners

## Slide 43: Trainings @ Software University (SoftUni)
Software University – High-Quality Education and Employment Opportunities
  softuni.bg
Software University Foundation
  http://softuni.foundation/
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg

## Slide 44: License
This course (slides, examples, demos, videos, homework, etc.) is licensed under the "Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International" license